## Slide 1: Lukas Pfitzenmaier, Pavlos Kollias, and Ulrich Löhnert Retrieving antenna miss-pointing for vertical pointing cloud radar and correcting the introduced Doppler velocity errors in the measurements
Doppler velocity from zenith pointing radars
Mean fall velocity of measured hydrometeors
No absolute calibration needed
Excellent information cloud microphysics and dynamics
Best quality Doppler velocity data
What is the velocity error due to antenna miss-pointing?
Can we monitor the radar pointing accuracy?
How to correct long time data sets?
Correction of historical measurements
Off zenith pointing
=> error in the Doppler velocity
Optimal case:
zenith pointing
Statistical method:
model winds (ECMWF IFS)
Doppler velocity data

## Slide 2: Lukas Pfitzenmaier, Pavlos Kollias, and Ulrich Löhnert Retrieving antenna miss-pointing for vertical pointing cloud radar and correcting the introduced Doppler velocity errors in the measurements
Statistical method
Bin Vm and Vh according to the wind direction
Calculate off-zenith pointing angles
Retrieve off-zenith pointing angle based on fit
EXAMPLE: Cross check
Correct Dual-Differential Doppler measurements
Ka-band
X-band
X-Ka-band
Dual Doppler
velocity
Correction of Dual-Differential Doppler velocity radar measurements
Correction of measurements
-> wind field (ECMWF IFS)
-> retrieved angle

## Slide 3: MATERIAL FOR DISCUSSION: Retrieving antenna miss-pointing for vertical pointing cloud radar and correcting the introduced Doppler velocity errors in the measurements
Lukas Pfitzenmaier, Pavlos Kollias, and Ulrich Löhnert

## Slide 4: Motivation:
fig. 2 from Mroz et.al, 2020
Control the quality of the Doppler Velocity data
Mean Doppler velocity is grate, because
  free from absolute calibration
  proportional to the hydrometeor fall velocities
Information about hydrometeor microphysics
  dual/triple Doppler velocity space (increasing data set)
  Input for retrievals
Satellite mission validation
  Aeolus and EarthCare
Provide best quality ground based Doppler velocity data
How big is the influence of off-zenith pointing antennas?
How can we monitor and correct the data?

## Slide 5: Retieval
How big is the influence of off-zenith pointing antennas?
How can we monitor and correct the data?
Error due to off-zenith pointing:
Proportional to mean horizontal wind speed, vh
Proportional to off-zenith pointing angle, 𝜙
Use of additional wind information:
ECMWF IFS data for wind (included in Cloudnet)
Possible to correct historical data
PPI scans to retrieve wind (available at JOYCE)
Long term wind statistic to retrieve off-zenith pointing angle based on sin-fit to data
=
=
Vm = Doppler velocity (measurement) Vh = mean horizontal wind speed Vv = mean vertical wind Speed Vp = mean particle fall velocity

## Slide 6: Results
Off-zenith pointing retrieved with ECMWF wind
  < 6 month wind statistics
Results compared to 𝜙 retrieved with sun scans are within 0.02° (Mai-June 2021)
Correction of past data sets based on retrieved angles and wind information (ECMWF or retrieved)
off-zenith pointing angle, 𝜙, time series
time series of azimuth pointing of 𝜙
Doppler velocity correction based on retrieved 𝜙 and additional wind information

## Slide 7: Results: Example Case 29-10-2020, JOYCE
retrieved wind dir
ECMWF
wind
retrieved wind
ECMWF
wind dir
Ka
band
X
band
X-Ka Doppler velocity
ECMWF based correction
& ECMWF wind field
ECMWF based correction
& retrieved wind field

## Slide 8: Results: Example Case 29-10-2020, JOYCE
X-Ka Doppler velocity
ECMWF based correction
& ECMWF wind field
ECMWF based correction
& retrieved wind field

## Slide 9: Conclusion:
Off zenith pointing can lead to error in the Doppler velocity
Estimation/Correction of the off-zenith pointing is estimated
  wind information
  Statistical method
Monitoring and Correction of the Doppler velocity is also possible for historical data sets

## Slide 10: BACKUP SLIDES: Retrieving antenna miss-pointing for vertical pointing cloud radar and correcting the introduced Doppler velocity errors in the measurements
Lukas Pfitzenmaier, Pavlos Kollias, and Ulrich Löhnert

## Slide 11
Input ECMWF IFS and PPI wind retrieval

## Slide 12
Final sun-fit to the data set to retrieve the angles,
apply a filter to get stabler estimates (95-5percentile data set & <2data bins)

## Slide 13
Das X-Band hatte relativ zum Mira ein mis-pointing von etwa 0.14° in N-S Richtung
Mira-36 um 0.08° korrikiert (mis-pointing maximum in O-W Richtung)

## Slide 14
Das X-Band hatte relativ zum Mira ein mis-pointing von etwa 0.14° in N-S Richtung
Mira-36 um 0.08° korrikiert (mis-pointing maximum in O-W Richtung)