## Slide 1: Using synthetic EarthCARE Cloud Profiling Radar data to develop validation methodologies for ground-based cloud radar sites What can we Learn From Synthetic CPR Data?
Lukas Pfitzenmaier1, Nils Risse1, Pavlos Kollias1,2,3,
Bernat Puigdomenech Treserras3, and Imke Schirmacher
1University of Cologne, Geophysics and Meteorology, Meteorology, Köln, Germany (l.pfitzenmaier@uni-koeln.de)
2Stony Brook University, School of Marine and Atmospheric Sciences, Stony Brook, NY, USA
3McGill University, Department of Atmospheric and Oceanic Science, Montreal, QC, Canada

## Slide 2: Motivation
Previous studies show (Rémillard & Tselioudis 2015, Lamer et al., 2020, Battaglia et al., 2020) :
detection of low (< 2km) clouds and precipitation is a challenge
  Clouds and precipitation overlapped by ground echo
  Low reflectivity of low cloud
  Clouds might be smaller than a satellite pixel
UoC operates W-band radars (JOYCE and NyÅlesund) within ACTRIS
  Continuous observations, homogeneous quality control
  Long term data sets for JOYCE (~ 15 years), NyAlesund (~ 5 years)
  Cover two climate zones
  ACTRIS target classification to filter data
Make use of these rich data sets for EarthCARE Cal/Val
  Develop a CPR forward simulator (within FRM4Radar and ACPV project)
  What can we learn from synthetic CPR data for EarthCARE Cal/Val?
NyÅlesund
JOYCE
ASKOS
campaign

## Slide 3: CPR forward simulator orbital-radar
INPUT: working on test data sets to test and present the tool:
transform suborbital radar data into synthetical CPR data
mimic the data sampling of CloudSat and EarthCARE
OUTPUT: synthetic CPR data in NetCDF
  Ze and Vm fields as a function of range and along-track
    Ze and Vm with and without noise
    Vm with and without velocity folding
Quality flags for
      multiple-scattering and
      Non-Uniform Beam Filling (NUBF)
      Doppler velocity folding
  GitHub: github.com/igmk/orbital-radar
  Paper ready and submission GMD is planned
in preperation

## Slide 4
Example: Synthetic CPR data, JOYCE, Jülich 6th April 2021
02.05.24
4
input: measured reflectivity
simulation: Doppler velocity + noise
Cloud boundaries are smoothed
Loosing low level cloud structures
ground echo
Doppler velocity is noisy because of
Sat motion,
low SNR
non-uniform-beam filling
High Ze will lead to multiple scattering!!
NUBF will introduce uncertainty
input: measured Doppler velocity
symulation: reflectivity + noise

## Slide 5
The homogeneous dataset from ACTRIS will enable the statistical comparison of ground vs space based cloud radar measurements
Statistics of ground based and synthetic CPR data – all data
FALLING
UP
FALLING
UP
JOYCE
5
velocity [m/s]
velocity [m/s]

## Slide 6
The homogeneous dataset from ACTRIS will enable the statistical comparison of ground vs space based cloud radar measurements (Protat et al., 2009, 2010, Kollias et al. 2019)
Farther: use the Cloudnet classification to group data
Statistics of ground based and synthetic CPR data – statistics
💧
💧
FALLING
UP
FALLING
UP
💧
💧
JOYCE
6
Filtering/classification of data is necessary to minimize attenuation influences
Long sampling time to generate robust statistics

## Slide 7
Space and time constraints to restrict comparable data (Protat et al., 2009, 2010, Kollias et al. 2019):
ground based data: +- 1 hour around the overpass time
From the satellite: all profiles with a 100 km radius around the site.
+ Cloudnet target classification & predicted overpasses – fixed no or CPR profiles & 2 h ground data
Statistics of ground based and synthetic CPR data – overpass simulation
JOYCE
NyÅlesund
💧
💧
💧
💧
Correlation Coefficient Ze ALL > 0.75 – NyÅlesund more than 50 Overpasses, JOYCE more than 100
Correlation Coefficient Vm ALL > 0.75 – NyÅlesund more than 300 overpasses (Joyce not enough data)
7
💧
💧
💧
💧
FALLING
FALLING
FALLING
FALLING
velocity [m/s]
velocity [m/s]
velocity [m/s]
velocity [m/s]

## Slide 8
Ground based radar network data are useful!
Their long term data sets can be used to understand CPR performance and develop methods Cal/Val pre launch
A possible tool to play around with data:
orbital-radar.py – github.com/igmk/orbital-radar
Compare ground-based to synthetical CPR data
estimate the sampling time for statistical comparison
Low level cloud remain challenging!
Farther work:
Improve cal/val of the Doppler velocity
Validate the syntenic CPR to EarthCARE CPR data
Summary:
8
very soon

## Slide 9: Jülich Observatory for Cloud Evolution (JOYCE)

## Slide 10
Additional slides: Example Synthetic CPR data, JOYCE, Jülich 6th April 2021
02.05.24
10
input: measured reflectivity
simulation: Doppler velocity + noise
Cloud boundaries are smoothed
Loosing low level cloud structures
ground echo
Doppler velocity is noisy because of
Sat motion,
low SNR
non-uniform-beam filling
High Ze will lead to multiple scattering!!
NUBF will introduce uncertainty
input: measured Doppler velocity
symulation: reflectivity + noise

## Slide 11: Additional slides: Example synthetic CPR quality control – MS and NUBF Have a look into the data quality and identify areas where data can be trusted!