## Slide 1
4. Observation: statistical analysis in 2010
6. Conclusions
Significantly enhanced PD (up to -10 K) during snowfall
 Existence of preferentially oriented snow particles
From observation & RT simulations:
 PD attenuated by LWP and enhanced by SWP
 TB enhanced by LWP and SWP
Potential of polarization observation for the improvement of retrieval algorithm
 Distinction between snow scattering and liquid emission
 Improvement of retrieval accuracy
1. Motivation
Reference:
Xie, X., U. Löhnert, S. Kneifel, and S. Crewell, 2012: Snow particle orientation observed by ground-based microwave radiometry, Journal of Geophysical research, 117, D02206, 12 pp., doi:10.1029/2011JD016369
2. Instrumentation
3. Observation: single snowfall case on 4th April 2010
Snow particle orientation observed by ground-based microwave radiometry
Xie, X., U. Löhnert, S. Kneifel, and S. Crewell
Institute for Geophysics and Meteorology, University of Cologne
2012 ICCP, Leipzig, Germany, 30.07-03.08, 2012
Acknowledgment:
The authors thank M. Mishchenko for providing the T-matrix code for public use and K. F. Evans for the radiative transfer model RT4 code package.
 Preferential orientation?
 Polarized signals?
DPR
Dual-Polarized microwave Radiometer (DPR)
150 GHz (vertical and horizontal polarizations) and 90 GHz
Sensitive to snow and liquid water
Humidity And Temperature PROfiler (HATPRO)
 Liquid water path (LWP) and integrated water vapor (IWV)
HATPRO
MRR
Micro Rain Radar (MRR)
 Integrated reflectivity factor
 Indirect snow water path (SWP)
Importance of snow in global energy budget and hydrological cycle
Dependence of retrieval accuracy on reasonable assumption of snow microphysical parameters
Limited knowledge on snow particle orientation
5. Radiative transfer simulation
Polarization observation at Umweltforschungsstation Schneefernerhaus (UFS, 2650 m MSL) on Mount Zugspitze, Germany
Snow duration: 11 UTC-19 UTC
Enhanced TB during snowfall
PD ~0 K at zenith
TBv<TBh off zenith
PD ~-10 K at 34.8o elevation
PD damped by LWP
TB enhanced by LWP
PD enhanced by SWP
TB enhanced by SWP
Brightness temperature
TB=(TBv+TBh)/2
Polarization difference
PD=TBv-TBh
TB and PD observed by DPR, and IWV and LWP derived from HATPRO
Indirectly measured SWP as a function of PD and TB at 34.8o elevation
LWP as a function of PD and TB at 34.8o elevation
Effects of snow parameters on PD
 Denser and flatter snow particles with horizontal orientation result in higher PD
Assumption of horizontally oriented snow oblates
Reconstructed atmospheric scenario in RT calculations
Effects of LWP and SWP on TB and PD are confirmed
Polarization observation is helpful for LWP and SWP retrievals
LWP mismatch is caused by different observation geometry
Dots indicate measurements during the snowfall case and colors specify LWP values from HATPRO.
DPR synergic observation with HATPRO and MRR