## Slide 1: Combined analysis of triple-frequency cloud radar and polarimetric X-Band radar observations of snow and ice microphysics
S. Kneifel, Davide Ori, J. Dias Neto, S. Trömel, R. Evaristo, J. Handwerker, B. Bohn
Notes: In this talk we will present recent activities adressing the question of how to study complex snow and ice cloud microphysical processes using a combination of multi-frequency cloud radar observations, Doppler spectral analysis and ‚classical‘ radar polarimetry.
The basis of this talk are measurements obtained during the first German triple-frequency field experiment which was made possible due to a collaboration between University of Cologne, Bonn, Research Center Jülich, and Karlsruhe Institute of Technology.

## Slide 2
Variability of snow and ice
Initial particle shape (plate, column, dendrite, rosette…)
Aggregation
Riming
These processes largely affect:
particle density
particle size distribution
terminal velocity
scattering properties (large uncertainties of single frequency radar retrievals)
T. Garret, U. Utah, Multi-angle snowflake camera
Notes: Probably, the best impression of the complexity and natural variability of particles we are facing in ice and snow clouds is given by this impressive particle images recorded with a recently developed snowflake camera.
Initial particle shapes like for example plates or needles are often altered by microphysical processes like aggregation or riming leading to a multitude of particle properties such as density, particle size distribution, and terminal velocity.
Of course, these physical particle properties also affect the way in which the particles interact with electromagnetic radiation. It is not surprising that this enormous variability causes large uncertainties in ice and snowfall radar retrievals, especially when only one radar frequency is available.

## Slide 3: Multi-frequency approach - Constraining the particle size distribution (PSD) utilizing different scattering regimes
Particle mass [mg]
Particle mass [mg]
Particle scattering properties change from Rayleigh to Mie depending on size/mass and frequency
Ku-band
W-band
Notes: This slide summarizes the basic idea of using mutli-frequency radar observations to constrain particle size distribution parameters.
The images show the backscattering cross section normalized by the particle mass for spherical particles. As long as we are in the Rayleigh scattering regime (as it is for example the case for snowflakes at the Ku-band), backscattering changes with mass squared.
At shorter wavelengths, we are enterring the complex Mie scattering regime. Backscattering is now a complex function of particle mass, wavelength and the particle‘s refractive index.

## Slide 4: Multi-frequency approach - Constraining the particle size distribution (PSD) utilizing different scattering regimes
Particle mass [mg]
Particle mass [mg]
Particle scattering properties change from Rayleigh to Mie depending on size/mass and frequency
Reflectivity is scattering integrated over all particle sizes (or masses)
Dual wavelength ratio: DWRKu, W = ZeKu – ZeW constrains PSD (rainfall, cirrus)
Ku-band
W-band
ZeKu > ZeW
Notes: Radar reflectivity is of course the sum of the backscattered radiation of all particles within a certain volume. If we look at the same particles at two wavelengths – as in this example Ku and W-band – we find a lower reflectivity at the wavelength which is already affected by Mie scattering.
This difference in reflectivities at two wavelengths is often denoted as the dual wavelength ratio (DWR) because in linear units the reflectivity difference becomes a ratio.
The DWR has been explored in the past for constraining effective size parameters of the PSD both for rainfall and ice clouds.

## Slide 5: Dual frequency approach – A sufficient solution also for snow particles?
Particle mass [mg]
Particle mass [mg]
Snow particle scattering depends also on particle shape
=> In order to constrain PSD we also have to constrain the shape
Can we achieve improvement if we combine 3 radar frequencies?
Ku-band
W-band
Notes: Similar to the plots from the previous slide, these two plots show again the backscattering cross section normalized with particles mass at Ku and W-band. For the different curves we used now various snow and ice scattering databases (black: single particles from the Liu database, green: aggregates also simulated with the discrete dipole approximation) but also classical approximations as Mie theory or T-Matrix.
While at Ku-band all particle models follow the Rayleigh approximation – as expected -, we see for W-band that the scattering curves seem not only depend on particle mass but also on the shape.

## Slide 6: Triple-frequency space: Simulations
Aggregates
Graupel
Oriented:
Plates
Dendrites
Several simulation studies showed that aggregates separate from single crystals and strongly rimed particles in the triple frequency space
Tyynelä and Chandrasekar, JGR, 2014
Kneifel et al., JGR, 2011
Notes: Kneifel and Coauthors calculated first the dual-wavelength ratios between Ku and Ka-band (y-axis) and Ka and W-band (x_axis) for a wide range of PSDs using various scattering databases and scattering approximations as just shown on the previous slides. Follow on studies, like those from Tyynelä and Chandrasekhar corroborated their findings.
Surprisingly, the approximations using spheres or spheroids with varying density and aspect ratio populate in a similar area in the triple-frequency space. The green lines, which represent DDA calculations for complex aggregates, however, reveal a ‚bending up‘ or ‚hook‘ feature as soon as the PSD includes an increasing number of larger particles.
The simulations imply that triple-frequency observations might indeed provide information about particle habit classes.

## Slide 7: Triple-frequency space: Observations
Kneifel et al., JGR, 2015
X, Ka, W Band radar observations
Collocated in-situ observations
Notes: Here, we show comparisons of the triple-frequency signatures from the lowest radar range gates (closest to the ground) to the ground-based in-situ observations from a recent field campaign in Hyytiälä, Finland. The case studies were carefully selected to ensure e.g. low wind speed conditions to make such a comparison feasible.
The left panels shows the observations from the three radars in the triple-frequency space for 6-minute periods. The color of the points denotes the mean Doppler velocities. The dashed black line indicates the average region in the triple-frequency space as predicted by spheroidal approximations. Its only intention is to guide the eye and to simplify a comparison to the simulation studies shown before.
The right panels show sample images of the snowflakes ground-based in-situ observations
At the beginning (uppermost panel) one finds mostly large and open-structured aggregates. Their triple-frequency signature shows clearly the bending-up signature predicted for such „fluffy“ aggregates.
At the end of the period we find smaller, and more rimed particles. Riming is evident in the steeper velocity-size distribution as well as in the general larger Doppler velocities (more dark blue colors). The triple-frequency signature is close to the „spheroidal“, dahsed black line and falls even below.
Similar signatures have been found in two other case studies of the same campaign. The results point out that the triple-frequency signature shows indeed sensitivity to particle habits and in particular to particle bulk density. This is clearly an added value compared to double-frequency observations which we aim to further explore in the near future. More details about the analysis and the two other case studies can be found in the cited reference.

## Slide 8
JOYCE site (Jülich, Germany)
KiXPOL (KIT)
JOYRAD-35
TRIPEx: First German triple frequency radar experiment
Winter 2015/16, Collaboration between U. Köln, U. Bonn, FZJ and KIT
JOYRAD-94
JuXPOL
Notes: Attempts to derive microphysical fingerprints of snow and ice clouds are constantly grown during recent years. The major radar observations used for this purpose are Radar polarimetry, Radar Doppler spectra, and multi-frequency radar.
While each area has ist specific fascination and challanges, we conducted a field experiment to better investigate the potential synergy of combining the different approaches.
In a collaborative initiative between University of Cologne, Bonn and Karlsruhe Institute of Technology, we installed three vertically pointing radars (X, Ka, and W-band) at the JOYCE supersite at the research center Jülich during winter months of 2015. JOYCE is surrounded by two polarimetric scanning X-Band radars, one 50km away in Bonn and a second one in only 4km distance.
In addition to the radars the site is equipped with a number of remote sensors including microwave radiometer, wind lidar and a radiosonde station.

## Slide 9: Golden Case: 24.11.2015
Notes: This slide shows the a frontal system passing over JOYCE on 24th November 2015.
The uppermost panel shows radar reflectivity of the 35 GHz radar, the middle panel the ceilometer backscatter signal, and the lowest panel the liquid water path derived from a collocated microwave radiometer.
During the first half of the day, the warm front approached with a slowly descending thick ice cloud. Both, the ceilometer and the MWR do only detect minimal amounts of super-cooled liquid water. During the second half of the day, the structure becomes much more complex in the cold frontal area.
In order to investigate the synergy of the different observations, we first analyszed a descending ice cloud caused by a warm front. No melting layer or precipitation on the ground was observed at that time.

## Slide 10: 24.11.2015, 10 - 11 UTC Multi-wavelength view
Ze-Ka
DWR-Ka-W
DWR-X-Ka
Offset and water vapor attenuation correction applied
Ze difference (DWR) between Ka and W band increases quickly below 4km
No significant amounts of liquid water (microwave radiometer)
No significantly enhanced Doppler velocity
Thus, riming is rather unlikely
What causes the DWR-Ka-W to increase?
Notes: The first panel shows time-height plot of reflectivity from one of the three vertically pointing radars. The lower two panels are difference plots of reflectivity between the two higher and the two lower frequencies. Initial corrections for water vapor attenuation and relative radar offsets have been applied (relative offsets have been determined from upper ice part for reflectivities below -10 dBz). Liquid water was not detected by the microwave radiometer during that time.
One finds a quickly increasing difference between Ka and W Band below an altitude of 4km. Only slightly increasing values are found for the X-Ka Band difference.
The zenith pointing radar and radiometer observations point towards an early onset of aggregation with particles still too small to cause a significant difference between X and Ka-band (based on the Finland results this means aggregate sizes smaller than ~8mm).

## Slide 11: 24.11.2015, 10 - 11 UTC Polarimetric view
JuXPOL
JOYCE
Notes: In addition to the vertically pointing multi-frequency radar observations, we also have polarimetric observations available from the nearby X-Band radar JuXPOL which perfomed RHI scans over the JOYCE site every 4 minutes. In the following we will concentrate on ZDR because the other variables like KDP were too noisy to draw definite conclusions.

## Slide 12
DWR-Ka-W
ZDR enhanced above the layer of increasing DWR-Ka-W
T = -15°C at 4.5km
Notes: At the beginning of the 1h time period, the dual wavelength ratios were in general small. However, ZDR is found to be anhanced between 3-4 km, just above the heights were the DWR-Ka-W slightly increases.
This is what we expect given that ZDR often depicts growth of plate-like particles such as dendrites which we expect to grow in this altitude range around -15°C.
Also it is reasonable that DWR-Ka-W increases just below since it is well known that dendrites very efficiently aggregate.

## Slide 13
DWR-Ka-W
Just 20 minutes later, ZDR signature almost completely dissappeared
Notes: The ZDR signatures becomes weaker if go forward in time. Interestingly, as the ZDR signature gets weaker, the underlying DWR signature increases indicating larger aggregates (but still smaller than appr. 8 mm due to non enhanced DWR-X-Ka!)

## Slide 14
DWR-Ka-W
Above layer of max. DWR-Ka-W the ZDR is very small
Notes: If we look into the time period of maximum DWR-Ka-W, the ZDR signature is barely visible anymore. This is difficult to understand given that we still believe that dendrites are growing in the layer above the DWR-Ka-W area.
Therefore, we will now also look into the Doppler spectra at this time from the vertically pointing Ka and W Band radars at JOYCE.

## Slide 15: 24.11.2015, 10:41 UTC Multi-Doppler view
No differential scattering above 5km (spectra well matched)
Increasing differential scattering clearly attributable to right (fast) side of the spectrum (aggregates)
RED: Ka-Band
BLUE: W-Band
Notes: The Doppler spectra from Ka-band (red) and W-Band (blue) are plottet between 2.5 and 5.5 km where we found the increase in Ka-W DWR.
At 5.5km, the spectra match quite well which is expected as long as the particles are Rayleigh scatterers at both frequencies and in every velocity bin. It is important to note that also the beam widths of the radars (0.6 and 0.45° for Ka and W-band, respectively) should be close in order to have similar turbulence broadening.
Further down we find the spectra to deviate from each other on the right (faster) falling side. This is expected since larger particles with larger fall velocities will first deviate from rayleigh scattering. Note that the DWR-Ka-W shown before is essentially the difference of the integrals of the two spectra.

## Slide 16: 24.11.2015, 10:41 UTC Multi-Doppler view
New small (slow) particle mode at 4.5km (T=-15°C, dendritic growth region)
New particle mode „speeds“ up and merges with aggregate mode around 1 m/s
Maximum of DWR-Ka-W is reached at 2.5-3 km where new mode almost completely merged with faster (aggregate) mode
RED: Ka-Band
BLUE: W-Band
Maximum DWR-Ka-W
Notes: The spectra become broader and slightly bimodal at 4.5 km. One can also see a slight shift of the spectra probably caused by a weak upward air motion. The bimodality points towards a new population of small, slowly falling ice particles. Whether these particles have been nucleated in this layer or are a result of seeding from above is difficult to judge. However, the temperature region of -15°C at 4.5km is well known to foster fast growth of plate-like, dendritic particles.
As soon as the initial slow second peak is getting faster, one can find an increasing differential scattering effect at the right (fast) side of the Doppler spectra. The Ka-band spectrum is constantly larger than the W-Band spectrum in accordance with Mie scattering effects. It is impressive that the spectra reveal a secondary population of growing particles before any differential scattering effect due to aggregation is found!
While the presented spectral evolution is for the time of largest DWR (around 10:40), the overall signature is impressingly stable in time.

## Slide 17: 24.11.2015, 10:41 UTC Multi-Doppler view
Interestingly, the weak ZDR signature appears at slightly lower height than the first bimodality in the spactra
Possibly, the asymmetric particles (dendrites) need to reach a certain size in order to become visible
The original aggregate mode seems to partly mask out the ZDR signal of the very first new particles
KDP values were very low during the entire hour (more related to particle concentration)
RED: Ka-Band
BLUE: W-Band
Maximum DWR-Ka-W
ZDR- layer
Notes: For easier comparison, we also indicate with the yellow box the altitude range were we found ZDR weakly enhanced. Interestingly, the spectra (also the ones from earlier periods) start to show the bimodality at higher levels where the ZDR is not yet showing any enhancement.
We suspect that the spectra are able to detect an early stadium of the dendritic particles while the particles need to grow further in size in order to contribute a significant signal to the total ZDR. Since the ZDR is derived as an average of all particles in the radar volume, we believe that the already existing aggregates are masking the newly formed particles.
The KDP signal is too weak to draw clear conclusions from it but also in KDP a slight enhancement below 4km seems at least to be consistent with our current picture of the microphysical processes.

## Slide 18: Conclusions
TRIPEx campaign allows combined analysis of triple-frequency moments, dual-frequency Doppler Spectra and nearby X-Band polarimetry
Strong multi-frequency signatures even in non-precipitating ice clouds
Spectra reveal bimodalities which are hard to detect using moments or polarimetry
Polarimetry indicates aspect ratio change (e.g. dendrites -> aggregates) but strong aggregate mode can obscure small particle signature
First analysis revealed additional information that can be gained by combining the three different methods.

## Slide 19: Additional slides

## Slide 20
Software artefact

## Slide 21: KDP

## Slide 22: KDP