## Slide 1: Attitude and Motion Correction for the HALO Cloud Radar
Martin Hagen

## Slide 2: Topic
Correction of Doppler velocity of HALO cloud radar to estimate vertical motions (fall speed + air motion) of cloud particles
Assessment of pointing errors of HALO cloud radar
  using return from earth surface
  using pitch, roll, ground-speed, vertical velocity of HALO
Understanding residual terms
  angular velocity (pitch rate, roll rate, yaw rate)
  precision of IRS/IGI velocities and angles
  accuracy of Doppler velocity from ground echoes
  timing issues

## Slide 3: Principle
HALO cloud radar is mounted fixed at the rear view-port looking downward
Cloud radar measures reflectivity of clouds and precipitation beneath HALO aircraft
DWD (PM) 1045 - 1130 Reflectivity
1045
1100
1115
1130

## Slide 4: Principle
Cloud radar measures only motion along radar beam, motion perpendicular to radar beam is not seen
  “Doppler velocity”
  “line-of-sight velocity”
what we see
HALO MIRA36 2013-12-19 11:31:48 – 10:46:29
w [m/s]

## Slide 5: Principle
Cloud radar measures only motion along radar beam, motion perpendicular to radar beam is not seen
  “Doppler velocity”
  “line-of-sight velocity”
what we want to see
HALO MIRA36 2013-12-19 11:31:48 – 10:46:29
w [m/s]

## Slide 6: Contribution of Aircraft Motion
Main contribution
  pitch
  ground speed (relevant for ground echo)
  true airspeed (relevant for clouds)
  vertical aircraft motion
Doppler velocity of ground echo should be zero vr = GS * sin(θ) = 210 m/s * sin(3°) = 10.99 m/s
Doppler velocity of ground is used to asses pointing direction of radar
Vground = 0
pitch
vertical aircraft velocity
TAS
GS
wind
pitch
θ

## Slide 7: Contribution of Aircraft Motion

## Slide 8: Contribution of Aircraft Motion

## Slide 9: Contribution of Aircraft Motion
and

## Slide 10: Contribution of Aircraft Motion
plus further (partly unknown) terms: angular velocities, SNR-radar, noise, …
ideal world
and

## Slide 11: Coordinate Systems
roll ϕ
pitch θ
flight ground track
longitudinal axis xa
lateral axis ya
normal axis za
horizon
north yg
south
west
up zg
projection of longitudinal axis xa to ground
radial velocity vr
east xg
heading ψ
drift
track
horizon

## Slide 12: Coordinate Systems: Transformations
angle between longitu-dinal axis and fixed earth reference system
Heading ψ
Pitch θ
angle between longitu-dinal axis and horizon
Roll ϕ
angle between lateral axis and horizon
θ
g
g
ψ
ϕ

## Slide 13: Pointing Direction of Cloud Radar
Doppler velocity vr is parallel to vaz and perpendicular to xa and ya vr = -vaz
evaluation of NARVAL 2013/2014 flights (73 segments 15-35 minutes from 6 research flights) indicates offsets from za
offset between IRS and IGI confirmed by A. Giez
vax
vay
vaz
vr
offset | pitch | roll
IRS | -0.24° | 0.09°
IGI | 0.18° | -0.02°

## Slide 14: Topic
Correction of Doppler velocity of HALO cloud radar to estimate vertical motions (fall speed + air motion) of cloud particles
Assessment of pointing errors of HALO cloud radar
  using return from earth surface
  using pitch, roll, ground-speed, vertical velocity of HALO
Understanding residual terms
  angular velocity (pitch rate, roll rate, yaw rate)
  precision of IRS/IGI velocities and angles
  accuracy of Doppler velocity from ground echoes
  timing issues

## Slide 15: Angular Velocity: Pitch Rate
range to surface changes when pitch is changing
pitch rate
r
h

## Slide 16: Angular Velocity: Pitch Rate
range to surface changes when pitch is changing
h = 12 km
pitch rate
r
h

## Slide 17: Doppler Velocity Noise
Radar receiver is close to saturation with return from surface
SNR of ground clutter is small
Spectral Width of ground clutter is wide; should be narrow
Doppler velocity of ground clutter has large uncertainty
additional spectral broadening by speed and pitch effects both spectra
-10 -5 0 5 10
velocity {m/s]
60
40
20
0
relative power [dB]
rain 90 m above surface
ground clutter
FFT 256 with pulses; averaged spectrum over 20 FFT PRF 5000 Hz -> 1.024 s
“clear air”

## Slide 18: Doppler Velocity of Ground Clutter
Range bin (28.8 m) with strongest echo is considered as ground clutter
NARVAL flight over sea towards low pressure system (changing altitude)
ground clutter +- 1 range bin
reflectivity [dB]
velocity[m/s]
spectr. w. [m/s]
range [m]

## Slide 19: Timing of Data
cloud radar samples FFT 256 with pulses; averaged spectrum over 20 FFT pulse rate PRF 5000 Hz  data rate 1.024 s
time stamp after averaged spectrum
PC uses HALO network time (synchronization ????)
BAHAMAS data
  pitch, roll, velocity average over last second
  pitch rate averaged over last second
time pitch pitch_rate vertical_velocity ground_speed
39048.450 3.57 -0.01 0.83 212.41
39049.450 3.54 -0.04 0.80 212.35
39050.450 3.45 -0.08 0.70 212.29
39051.450 3.44 -0.01 0.55 212.24

## Slide 20: Conclusion
Correction of Doppler velocity of HALO cloud radar to estimate vertical motions (fall speed + air motion) of cloud particles is possible
Retrieval of vertical velocities in clouds and precipitation requires knowledge of wind profile
Residual terms due to
  precision of IRS/IGI velocities and angles
  accuracy of Doppler velocity from ground echoes
  timing issues
    need BAHAMAS data with higher data rate (10 Hz)
    higher data rate for radar data (?? storage issue on radar computer ??)
Future option: adjust average pitch (2.5 – 3°) at radar antenna (also for radiometer, WALES)